## Slide 1: TCP/IP and OSI
Business Data Communications

## Slide 2: What is a Protocol?
Allows entities (i.e. application programs) from different systems to communicate
Shared conventions for communicating information are called protocols
Includes syntax, semantics, and timing

## Slide 3: Why Use Protocol Architecture?
Data communications requires complex procedures
  Sender identifies data path/receiver
  Systems negotiate preparedness
  Applications negotiate preparedness
  Translation of file formats
For all tasks to occur, high level of cooperation is required

## Slide 4: Modular Approach
Breaks complex tasks into subtasks
Each module handles specific subset of tasks
Communication occurs
  between different modules on the same system
  between similar modules on different systems

## Slide 5: Advantages of Modularity
Easier application development
Network can change without all programs being modified

## Slide 6: Three-Layer Model
Distributed data communications involves three primary components:
  Networks
  Computers
  Applications
Three corresponding layers
  Network access layer
  Transport layer
  Application layer

## Slide 7: Network Access Layer
Concerned with exchange of data between computer and network
Includes addressing, routing, prioritizing, etc
Different networks require different software at this layer
Example: X.25 standard for network access procedures on packet-switching networks

## Slide 8: Transport Layer
Concerned with reliable transfer of information between applications
Independent of the nature of the application
Includes aspects like flow control and error checking

## Slide 9: Application Layer
Logic needed to support various applications
Each type of application (file transfer, remote access) requires different software on this layer

## Slide 10: Addressing
Each computer on a network requires a unique address on that network
Each application requires a unique address within the computer to allow support for multiple applications (service access points, or SAP)

## Slide 11: Data Transmission
Application layer creates data block
Transport layer appends header to create PDU (protocol data unit)
  Destination SAP, Sequence #, Error-Detection Code
Network layer appends another header
  Destination computer, facilities (e.g. “priority”)
See figure 4.5 in the book

## Slide 12: Simplified Architecture

## Slide 13: Protocol Architecture Operation

## Slide 14: Standardized Protocol Architectures
Vendors like standards because they make their products more marketable
Customers like standards because they enable products from different vendors to interoperate
Two protocol standards are well-known:
  TCP/IP: widely implemented
  OSI: less used, but widely known and still useful for modeling/conceptualizing

## Slide 15: TCP/IP
Transmission Control Protocol/Internet Protocol
Developed by DARPA
No official protocol standard
Identifies 5 Layers
  Application
  Host-to-Host (transport)
  Internet
  Network Access
  Physical

## Slide 16: TCP/IP Physical Layer
Physical interface between a DTE (e.g. computer or terminal) and a transmission medium
Specifies:
  Characteristics of medium
  Nature of signals
  Data rate

## Slide 17: TCP/IP Network Access
Exchange of data between systems on a shared network
Utilizes address of host and destination
Can also prioritize transmission
Software at this layer depends on network (e.g. X.25 vs. Ethernet)
Segregation means that no other software needs to be concerned about net specifics

## Slide 18: TCP/IP Internet Layer
An Internet is an interconnection of two or more networks
Internet layer handles tasks similar to network access layer, but between networks rather than between nodes on a network
Uses IP for addressing and routing across networks
Implemented in workstations and routers

## Slide 19: TCP/IP Transport Layer
Also called host-to-host layer
Reliable exchange of data between applications
Uses TCP protocols for transmission

## Slide 20: TCP/IP Application Layer
Logic needed to support variety of applications
Separate module supports each type of application (e.g. file transfer)

## Slide 21: TCP & UDP
Most TCP/IP applications use TCP for transport layer
TCP provides a connection (logical association) between two entities to regulate flow check errors
UDP (User Datagram Protocol) does not maintain a connection, and therefore does not guarantee delivery, preserve sequences, or protect against duplication

## Slide 22: IP and IPv6
IP provides for 32-bit source and destination addresses
IPv6 (1996 standard) provides for 128-bit addresses
Migraqtion to IPv6 will be a very slow process

## Slide 23: TCP/IP Applications
SMTP (Simple Mail Transfer Protocol)
  Basic e-mail facility, transferring messages among hosts
FTP (File Transfer Protocol)
  Sends files from one system to another on user command
Telnet
  Remote login capability, allowing a user to emulate a terminal on the remote system

## Slide 24: Internetworking
Interconnected networks, usually implies TCP/IP
Can appear to users as a single large network
The global Internet is the largest example, but intranets and extranets are also examples

## Slide 25: Routers
Equipment used to interconnect independent networks
Several essential functions
  Provide a link between networks
  Provide routing and delivery of data between processes on systems from different networks
  Provide the above functions without requiring modification of the attached networks

## Slide 26: Router Issues
Addressing schemes
Maximum packet size
Interfaces
Reliability

## Slide 27: TCP Segment (TCP PDU)
Source port (16 bits)
Destination port (16 bits)
Sequence number (32 bits)
Acknowledgment number (32 bits)
Data Offset (4 bits)
Reserved (6 bits)
Flags (6 bits) : URG, ACK, PSH, RST, SYN, FIN
Window (16 bits)
Checksum (16 bits)
Urgent Pointer (16 bits)
Options (variable)

## Slide 28: IPv4 Header
Version (4 bits)
Internet header length (4 bits)
Type of Service (8 bits)
Total Length (16 bits)
Identification (16 bits)
Flags (3 bits
Fragment Offset (13 bits)
Time to Live (8 bits)
Protocol (8 bits
Header Checksum (16 bits)
Source Address ( 32 bits)
Destination Address (32 bits)
Options (variable)
Padding (variable)

## Slide 29: Why Study OSI?
Still an excellent model for conceptualizing and understanding protocol architectures
Key points:
  Modular
  Hierarchical
  Boundaries between layers=interfaces

## Slide 30: OSI
Open Systems Interconnection
Developed by ISO
Contains seven layers (see page 358)
Application
Presentation
Session
Transport
Network
Data Link
Physical

## Slide 31: OSI Lower Layers
Physical
Data Link
Network

## Slide 32: OSI Physical Layer
Responsible for transmission of bits
Always implemented through hardware
Encompasses mechanical, electrical, and functional interfaces
e.g. RS-232

## Slide 33: OSI Data Link Layer
Responsible for error-free, reliable transmission of data
Flow control, error correction
e.g. HDLC

## Slide 34: OSI Network Layer
Responsible for routing of messages through network
Concerned with type of switching used (circuit v. packet)
Handles routing between networks, as well as through packet-switching networks

## Slide 35: OSI Upper Layers
Transport
Session
Presentation
Application

## Slide 36: OSI Transport Layer
Isolates messages from lower and upper layers
Breaks down message size
Monitors quality of communications channel
Selects most efficient communication service necessary for a given transmission

## Slide 37: OSI Session Layer
Establishes logical connections between systems
Manages log-ons, password exchange, log-offs
Terminates connection at end of session

## Slide 38: OSI Presentation Layer
Provides format and code conversion services
Examples
  File conversion from ASCII to EBDIC
  Invoking character sequences to generate bold, italics, etc on a printer

## Slide 39: OSI Application Layer
Provides access to network for end-user
User’s capabilities are determined by what items are available on this layer

## Slide 40: TCP/IP - OSI Comparison